## Slide 1
FreshGuard
Early Spoilage Detection & Supply-Chain Evidence Platform
A ₹4,000 device that brings cold-chain intelligence to the ordinary trucks that carry most of India's produce — and creates the evidence that decides who pays for the loss.
Team BIO SENTINEL
Track — AI / ML, IoT, Smart Sensor, Industrial Automation
DeepTech Hackathon 2026
Notes: FreshGuard — early spoilage detection and supply-chain evidence platform. Team BIO SENTINEL.

## Slide 2
PROBLEM
Spoilage is discovered at the one moment when nothing can be done about it.
₹31,486 Cr
Lost every year to post-harvest damage in fruits and vegetables alone
5 – 15%
Of India's fruit and vegetable output is lost after harvest
(guava >15%, tomato ~12%)
10,000 / 62,000
Refrigerated trucks India has, against the number it needs
Pain Points
Damage is found when the doors open — after payment, after transport, with no time to act.
No record of when, where or under whose custody produce degraded, so losses cannot be attributed or claimed.
Buyers absorb spoilage caused by suppliers, because after a nine-hour journey both look identical.
Refrigeration is not a reachable answer — projections reach only ~33,000 reefer vehicles by 2031.
Why Existing Solutions Fall Short
Built for refrigerated vehicles — the small minority of produce freight.
They log temperature, a lagging proxy that reports conditions, not the state of the food.
Fixed thresholds set in a lab require per-vehicle commissioning and recalibration — impractical at fleet scale.
Unit costs of ₹25,000+ put them out of reach of small transporters and aggregators.
Sources: NABCONS post-harvest loss study (presented to Parliament, 2024); ICAR-CIPHET (2015); NCCD / NABCONS cold-chain infrastructure assessment.
Notes: Lead with the reefer gap: you cannot refrigerate five million trucks.

## Slide 3
SOLUTION
One ₹4,000 device. Four business outcomes — only one of which is detection.
1
Reject bad cargo at the dock
FreshGuard validates its own baseline against clean-air limits. Produce already degrading when loaded is flagged within two minutes — while the supplier is still present and the batch can still be refused.
2
Warn the destination in transit
Live gas, humidity and door telemetry streams to a dashboard, so the receiving warehouse knows a load is deteriorating hours before it arrives and can prepare for it.
3
Sequence warehouse outbound
Consignments are ranked by measured condition, so the stock closest to the edge is distributed first — the same spoilage, but far less revenue lost to it.
4
Attribute the loss with evidence
Every reading is signed on-device and hash-chained into a tamper-evident timeline, turning an unwinnable argument into a documented fact.
What makes it possible
FreshGuard sets no fixed thresholds. It measures the air inside the container at shipment start, adopts it as that trip's baseline, and alerts on deviation — with a commodity profile selected at loading. This eliminates per-vehicle field calibration, so the sensing works in vehicles nobody will ever service.
Notes: Only outcome 1 is detection. Outcomes 2-4 are operational and commercial.

## Slide 4
COMPETITIVE ADVANTAGE
Existing products monitor the refrigerated minority and need calibrating. We serve the majority and calibrate ourselves.
 | Conventional cold-chain trackers | FreshGuard
Target vehicle | Refrigerated trucks only (~10,000 in India) | Any goods vehicle, refrigerated or not
What is sensed | Temperature — a lagging proxy | Volatile compounds — direct evidence of decay
Threshold model | Fixed limits set in a laboratory | Self-captured baseline, every single trip
Commissioning | Per-vehicle setup by a technician | None — fit it and close the doors
Quality at origin | Not detected | Flagged within ~2 minutes of loading
Evidence trail | Temperature log, editable | Signed, hash-chained, tamper-evident
Indicative cost | ₹25,000+ | ~₹4,000
Recovers margin, not just waste
Recovering one percentage point of an 8% loss on ₹50 crore of produce is ₹50 lakh a year — against ₹4 lakh of hardware for a 100-truck fleet.
Turns loss into leverage
Separates loss the buyer caused from loss the buyer was sold, creating supplier accountability that compounds every season.
Deploys where nothing else can
Zero commissioning means fitting 1,000 vehicles costs the same per unit as fitting one.
Notes: Business value in the buyer's language: margin, leverage, deployability.

## Slide 5
BUSINESS MODEL
Hardware gets us in the vehicle. The evidence record is what makes us hard to remove.
Revenue Model
Stream | What the customer gets | Indicative pricing
Hardware | One-time device sale, per vehicle | ₹7,000 – 9,000
SaaS subscription | Dashboard, live monitoring, alerts | ₹300 – 500 / vehicle / month
Enterprise licensing | On-premise deployment for large aggregators and retail chains | Annual licence
Evidence & compliance | Exportable custody records for disputes, insurance and food-safety audit | Per-report or bundled
Premium analytics | Supplier quality scorecards and route-risk reporting | Add-on tier
Our first customer
The buyer / distributor — the party that today absorbs losses it did not cause. Outcomes 1 and 4 pay them directly.
Why customers stay
Once supplier contracts reference FreshGuard records, switching is not a data migration — it is a renegotiation. Evidence becomes authoritative only once both sides accept it, and that position compounds.
Why this model works
Because the device needs no commissioning, it sells through distribution rather than field engineers. A transporter can buy one, fit it, and be operational the same day.
Future Revenue
Fleet learning
Baselines pooled across shipments to learn each commodity's normal profile
Supplier scoring
Reliability ratings sold to buyers, built from accumulated origin-quality flags
Shelf-life prediction
Remaining-hours estimation, pending experimental validation
Insurance partnerships
Verified custody records underwriting spoilage cover
Notes: First customer is the buyer/distributor. Fleet learning and shelf-life are roadmap, not current capability.

## Slide 6
TRACTION
A working device, a live pipeline, and a spoilage response we have measured ourselves.
Completed
Working ESP32 prototype — gas (MQ135), humidity and door sensing operational
Self-baselining implemented: warm-up, clean-air capture, deviation detection
Spoilage response verified on the bench — a sealed cut-onion sample produces a clear, repeatable rise against baseline
End-to-end telemetry live: ESP32 → Next.js API → Supabase → dashboard, posting every 3 seconds
Web dashboard deployed with per-vehicle views and alert states
On-device OLED display and local buzzer alerting
Validated Performance
Baseline capture completes within ~2 minutes of power-on
Clear, repeatable separation between clean-air baseline and a spoilage-proxy sample
Gas channel returns to baseline after exposure — confirming continuous measurement rather than threshold latching
Telemetry chain confirmed reliable end-to-end under live network conditions
Selected for the finals of a prior hackathon on this concept
Next Steps
Multi-hour spoilage trials across tomato, onion and leafy greens to characterise deviation curves
Calibrate the clean-air sanity band driving the origin-quality alert
Commodity Mode profiles for the first four crops
Signed, hash-chained record format and exportable cargo certificate
Migrate to a digital VOC sensor (SGP30 / BME680) for stability and manufacturability
Pilot deployment with a regional produce transporter
Demonstrable live
Every item under Completed can be shown working at our booth — including the gas channel rising and returning to baseline against a sealed sample, in real time.
Notes: Everything under Completed is demonstrable at the booth.

## Slide 7
GO TO MARKET STRATEGY
Land with the party that pays for the loss, then expand across their supplier network.
Target Customers
Fruit and vegetable aggregators and mandi-level wholesalers
Regional transport operators running unrefrigerated fleets
Farmer Producer Organisations shipping to distant markets
Organised retail and quick-commerce grocery chains
Dairy collection and distribution networks
Customer Acquisition
Paid pilots with two or three regional aggregators, priced at hardware cost in exchange for route data
Loss-reduction case studies from those pilots as the primary sales asset
Partnerships with FPOs and agri-cooperatives for bundled distribution
Live demonstrations at agri and cold-chain trade exhibitions
Customer Retention
The dashboard becomes the operational record of every shipment
Supplier scorecards accumulate value over time and cannot be transferred to a competitor
Continuous firmware and model improvements delivered over the air
Responsive support for a segment unaccustomed to receiving any
Sales & Marketing Channels
Direct B2B sales to aggregators and fleet operators
Channel sales through existing vehicle-telematics and GPS-tracker dealers, who already sell to this exact customer
Agri and cold-chain expos, FPO networks
Government cold-chain and post-harvest schemes as a subsidy route for buyers
Notes: First customer: the buyer/distributor. Telematics dealer channel is the fastest route to volume.