## Slide 1
FreshGuard
Early Spoilage Detection & Supply-Chain Evidence Platform
Refrigeration proves the truck was cold. It cannot prove the food is still good. FreshGuard measures the cargo itself — and creates the evidence that decides who pays when a load is lost.
Team BIO SENTINEL
Track — AI / ML, IoT, Smart Sensor, Industrial Automation
DeepTech Hackathon 2026
Notes: FreshGuard — early spoilage detection and supply-chain evidence platform. Team BIO SENTINEL.

## Slide 2
PROBLEM
A refrigerated truck can hold 4°C the whole way and still deliver spoiled cargo.
₹31,486 Cr
Lost every year to post-harvest damage in fruits and vegetables alone
5 – 15%
Of India's fruit and vegetable output is lost after harvest
(guava >15%, tomato ~12%)
$12.6B → $27.4B
India's cold-chain transport market by 2034 — more perishable cargo in transit every year, monitored only by temperature
Pain Points
Refrigeration slows decay; it does not stop it. Cargo loaded already degrading arrives spoiled despite a perfect temperature log.
Damage is found when the doors open — after payment, after transport, with no time to act.
No record of when, where or under whose custody produce degraded, so losses cannot be attributed or claimed.
Buyers absorb spoilage their suppliers caused, because after a nine-hour journey good and poor consignments look identical.
Why Existing Solutions Fall Short
They answer "was the truck cold enough?" — never "is the cargo still good?"
Temperature is a lagging proxy. It reports conditions, not the state of the food.
Fixed thresholds set in a lab need per-vehicle commissioning and recalibration — impractical across a fleet.
Temperature logs are editable, so they settle no dispute about who caused a loss.
Sources: NABCONS post-harvest loss study, presented to Parliament 2024 · ICAR-CIPHET (2015) · IMARC Group, India Cold Chain Transport Market 2025–2034 · NCCD / NABCONS cold-chain capacity assessment
Notes: Core line: temperature compliance is not the same as freshness. A perfect cold log and spoiled cargo are entirely compatible.

## Slide 3
SOLUTION
Measure the cargo, not just the container. Four business outcomes — only one of them is detection.
1
Reject bad cargo at the dock
FreshGuard validates its own baseline against clean-air limits. Produce already degrading when loaded is flagged within two minutes — while the supplier is still present and the batch can still be refused.
2
Warn the destination in transit
Live gas, humidity and door telemetry streams to a dashboard, so the receiving warehouse knows a load is deteriorating hours before it arrives and can prepare for it.
3
Sequence warehouse outbound
Consignments are ranked by measured condition, so the stock closest to the edge is distributed first — the same spoilage, but far less revenue lost to it.
4
Attribute the loss with evidence
Every reading is signed on-device and hash-chained into a tamper-evident timeline, turning an unwinnable argument into a documented fact.
What makes it possible
FreshGuard sets no fixed thresholds. It measures the air inside the container at shipment start, adopts it as that trip's baseline, and alerts on deviation — with a commodity profile selected at loading. The refrigerated environment is what makes this precise: a sealed volume lets spoilage gases accumulate, forced air circulation carries them to the sensor, and a stable 4°C removes the temperature drift that would otherwise corrupt the reading.
Notes: Only outcome 1 is detection. Outcomes 2-4 are operational and commercial.

## Slide 4
COMPETITIVE ADVANTAGE
Every competitor measures the container. We measure what is inside it.
 | Conventional cold-chain trackers | FreshGuard
Question answered | "Was the truck cold enough?" | "Is the cargo still good?"
What is sensed | Temperature — a lagging proxy | Volatile compounds — direct evidence of decay
Threshold model | Fixed limits set in a laboratory | Self-captured baseline, every single trip
Commissioning | Per-vehicle setup by a technician | None — fit it and close the doors
Quality at origin | Not detected | Flagged within ~2 minutes of loading
Evidence trail | Temperature log, editable | Signed, hash-chained, tamper-evident
Indicative unit cost | ₹25,000+ | ₹14,000 – 16,000
Recovers margin, not just waste
Recovering one percentage point of an 8% loss on ₹50 crore of produce is ₹50 lakh a year — against ₹15 lakh to equip a 100-vehicle fleet.
Turns loss into leverage
Separates loss the buyer caused from loss the buyer was sold, creating supplier accountability that compounds every season.
Scales without technicians
Zero commissioning means equipping 1,000 vehicles costs the same per unit as equipping one — the barrier that keeps monitoring off most of the fleet today.
Notes: Business value in the buyer's language: margin, leverage, deployability.

## Slide 5
BUSINESS MODEL
Hardware gets us into the cold chain. The evidence record is what makes us hard to remove.
Revenue Model
Stream | What the customer gets | Indicative pricing
Hardware | One-time device sale, per vehicle | ₹14,000 – 16,000
SaaS subscription | Dashboard, live monitoring, alerts | ₹1,000 / vehicle / month
Enterprise licensing | On-premise deployment for large aggregators and retail chains | Annual licence
Evidence & compliance | Exportable custody records for disputes, insurance and food-safety audit | Per-report or bundled
Premium analytics | Supplier quality scorecards and route-risk reporting | Add-on tier
Our first customer
Cold-chain logistics operators and the buyers they serve — the parties that today absorb losses they did not cause. Outcomes 1 and 4 pay them directly.
Why customers stay
Once supplier contracts reference FreshGuard records, switching is not a data migration — it is a renegotiation. Evidence becomes authoritative only once both sides accept it, and that position compounds.
Why this model works
Because the device needs no commissioning, it sells through distribution rather than field engineers. A transporter can buy one, fit it, and be operational the same day.
Future Revenue
Cold storage chambers
Same device in static cold rooms — 8,000+ facilities, where produce sits for weeks
Supplier scoring
Reliability ratings sold to buyers, built from accumulated origin-quality flags
Fleet learning
Baselines pooled across shipments to learn each commodity's normal profile
Insurance partnerships
Verified custody records underwriting spoilage cover
Notes: First customer is the buyer/distributor. Fleet learning and shelf-life are roadmap, not current capability.

## Slide 6
TRACTION
A working device, a live pipeline, and a spoilage response we have measured ourselves.
Completed
Working ESP32 prototype — gas (MQ135), humidity and door sensing operational
Self-baselining implemented: warm-up, clean-air capture, deviation detection
Spoilage response verified on the bench — a sealed cut-onion sample produces a clear, repeatable rise against baseline
End-to-end telemetry live: ESP32 → Next.js API → Supabase → dashboard, posting every 3 seconds
Web dashboard deployed with per-vehicle views and alert states
On-device OLED display and local buzzer alerting
Validated Performance
Baseline capture completes within ~2 minutes of power-on
Clear, repeatable separation between clean-air baseline and a spoilage-proxy sample
Gas channel returns to baseline after exposure — confirming continuous measurement rather than threshold latching
Telemetry chain confirmed reliable end-to-end under live network conditions
Selected for the finals of a prior hackathon on this concept
Next Steps
Multi-hour spoilage trials across tomato, onion and leafy greens to characterise deviation curves
Calibrate the clean-air sanity band per commodity, driving the origin-quality alert
Commodity Mode profiles for the first four crops, plus temperature/humidity compensation of the gas channel
Signed, hash-chained record format and exportable cargo certificate
Migrate to Figaro TGS2600 for ethylene-specific sensing, closing the ripening gap
Pilot deployment with a regional produce transporter
Demonstrable live
Every item under Completed can be shown working at our booth — including the gas channel rising and returning to baseline against a sealed sample, in real time.
Notes: Everything under Completed is demonstrable at the booth.

## Slide 7
GO TO MARKET STRATEGY
Land with the party that pays for the loss, then expand across their supplier network.
Target Customers
Cold-chain logistics operators running reefer fleets
Quick-commerce and organised retail grocery cold chains
Dairy collection and distribution networks
Fruit and vegetable exporters meeting import quality standards
Cold storage operators and packhouses
Customer Acquisition
Paid pilots with two or three cold-chain operators, priced at hardware cost in exchange for route data
Loss-reduction case studies from those pilots as the primary sales asset
India's cold-chain transport market is growing ~8.6% a year and the reefer fleet is projected to triple by 2031 — every new vehicle is a new install
Live demonstrations at agri and cold-chain trade exhibitions
Customer Retention
The dashboard becomes the operational record of every shipment
Supplier scorecards accumulate value over time and cannot be transferred to a competitor
Continuous firmware and model improvements delivered over the air
Responsive support for a segment unaccustomed to receiving any
Sales & Marketing Channels
Direct B2B sales to aggregators and fleet operators
Channel sales through existing vehicle-telematics and GPS-tracker dealers, who already sell to this exact customer
Agri and cold-chain expos, FPO networks
Government cold-chain and post-harvest schemes as a subsidy route for buyers
Notes: First customer: cold-chain operators. Telematics dealer channel is the fastest route to volume.